## Slide 1
Nechako Reservoir / River / Freshet Information Sharing –
Community Leaders
Prepared by Andrew Czornohalan & Water Resources Group
06 March 2024

## Slide 2: Current Snowpack

## Slide 3: Current Snowpack
249 mm (65% LTA)
3rd lowest in 66 years

## Slide 4: Reservoir Elevation - Last 20 days
Current reservoir level
2789.61 ft

## Slide 5: Flows - Last 30 days
Current values (m³/s) | 
Vanderhoof | 39
Skins Lake | 33
Cheslatta Falls | 34
Nautley | 5
Stellako | 3
All streamflows values are provisional and subject to ice effects.
Notes: Keep in mind:
River Discharge measurements are estimated from water level,
Skins Lake Spillway discharge are estimated from gate opening.
Graphique dans: ProcessBook->Hydrological Data -> Kemano & Nechako River Discharge ->Nechako at Vanderhoof

## Slide 6: Observed Water Temperatures – Last 15 days
Average – Last 24h (°C) | 
Below spillway | 17.1
Cheslatta Falls | 17.7
Fort Fraser | 17.8
Nautley River | 18.8
Vanderhoof | 18.3
Finmoore | 18.2
Target : <20°C daily average at Finmoore

## Slide 7: Past & Future total precipitation
Observation (last month)
Nechako Reservoir watershed area-average = 29 mm
Historical Average = 69 mm
Nechako Reservoir watershed area-average = 15-20 mm
Forecast (next 7 days)

## Slide 8: Weather Forecast
Marilla Weather

## Slide 9: Weather Forecast*
*Possible Weather Stations
Nechako Reservoir
Kemano
Streatham
Marilla
Leon 14
Nechako River
Vanderhoof
McDonalds Landing
Streatham
Baptiste Louis 8
Leon 14
Marilla
Targe Creek
Burns Lake Weather
Cheslatta
Baptiste Louis 8
Targe Creek
Nautley
McDonalds Landing
Burns Lake
Fraser Lake

## Slide 10: Provincial Advisories - Drought
Source: British Columbia Drought Information Portal
Water Management Branch – Ministry of Forests
Last updated : 30-Nov.
Drought Level 3 : Adverse Impacts Possible
North Lucas Lake
Tatuk Lake
Drought updates have concluded for the 2023 season and will resume in spring 2024.
Wide Basins & Imperfect borders
The Stellako River : Upper Fraser West (level 4)
Western portions of Burkley Lakes saw higher flows
Several indicators are factored : see Plan.
British Columbia Drought and Water Scarcity Response Plan (gov.bc.ca)
https://www2.gov.bc.ca/assets/gov/environment/air-land-water/water/drought-info/drought_response_plan_final.pdf
Notes: drought levels are a general condition across what are quite often large basins
the borders of these basins are imperfect
The Stellako River, which drains into Francois Lake) has a hydrometric station at Glenannan, which is located in the Upper Fraser West basin.
During the month of November, the areas in the western portion of the Bulkley-Lakes Basin were experiencing higher flows

## Slide 11: Provincial Advisories - Flood
Source: BC River Forecast Center.
Last updated : May 23th 2023

## Slide 12: Observed Inflows & Discharge vs Historical

## Slide 13: Spring Freshet Inflow Volume Forecast
Historical Record of Observed Volumes
Forecast Volume Exceedance Probability
Forecast Volume Average
Last year
72% LTA

## Slide 14: Nautley River Flows, Forecast
Notes: Spike on natural inflows (max) Is 2007.

## Slide 15: Vanderhoof
Source: 08JC001 NECHAKO RIVER AT VANDERHOOF (gov.bc.ca)

## Slide 16: Skins Lake Spillway Release - Forecast
Current release = 33 m³/s

## Slide 17: Forecast – Vanderhoof
Source : RFC's Clever model - 08JC001.PDF(gov.bc.ca)

## Slide 18: Reservoir Level Projection

## Slide 19: Updates - Next Steps – Actions
Confirm next meeting date & time – Propose April 3rd
Work with BC Hydro to manage the drought and energy balance for the winter
Report out Dam Safety Review and Dam Emergency Plan once updated in Spring
Presentations are available on the Get Involved Nechako website under 'Our Operations'. Recordings can be requested up to 30 days following the meeting.

## Slide 20
Flow facts of last Thursday

## Slide 21
Feedback & Reflections